## Slide 1: ORTHOGRAPHIC PROJECTIONS OF POINTS, LINES & PLANES

## Slide 2: Projection
The task of recording the shapes and sizes of 3-D objects on 2-D drawings in done using Projections.
Orthographic projection: When the projectors are parallel to each other and also perpendicular to the plane, the projection is called orthographic projection.
Method of obtaining orthographic views (top view and front view)

## Slide 3: To draw projections of any object, one must have following information:
A) OBJECT
{With its description, well defined}
B) OBSERVER
{Always observing perpendicular to resp. Ref. Plane}
C) LOCATION OF OBJECT
{Means its position with reference to H.P. & V.P.}

## Slide 4
NOTATIONS
Following notations should be followed while naming
Different views in orthographic projections.
IT’S FRONT VIEW a´ a´ b´
Same system of notations should be followed
incase numbers, like 1, 2, 3 – are used.
OBJECT POINT A LINE AB
IT’S TOP VIEW a a b
IT’S SIDE VIEW a´´ a´´ b´´
TERMS ‘ABOVE’ & ‘BELOW’ WITH RESPECT TO H.P.
AND TERMS ‘INFRONT’ & ‘BEHIND’ WITH RESPECT TO V.P.

## Slide 5
X
Y
1st Quadrant
2nd Quadrant
3rdQuadrant
4th Quadrant
F.V.
1ST Quad.
2nd Quad.
3rd Quad.
4th Quad.
X Y
Observer
VP
HP
Observer
This quadrant pattern, if observed along x-y line (in red arrow direction) will exactly appear as shown on right side and hence it is further used to understand illustration properly.

## Slide 6
HP
VP
a´
a
A
POINT A IN
1ST QUADRANT
OBSERVER
VP
HP
POINT A IN
2ND QUADRANT
OBSERVER
a´
a
A
OBSERVER
a
a´
POINT A IN
3RD QUADRANT
HP
VP
A
OBSERVER
a
a´
POINT A IN
4TH QUADRANT
HP
VP
A
Point A is
placed In
different
quadrants
and it’s FV & TV
are brought in
same plane for
Observer to see
clearly.
FV is visible as
it is a view on
VP. But as TV is
is a view on HP,
it is rotated
900,
in clockwise
direction. The
front part of
HP comes below
XY line and the
part behind VP
comes above.

## Slide 7
A
a
a´
A
a
a´
A
a
a´
X
Y
X
Y
X
Y
For FV
For TV
For FV
For TV
For TV
For FV
POINT A ABOVE HP
& INFRONT OF VP
POINT A IN HP
& INFRONT OF VP
POINT A ABOVE HP
& IN VP
PROJECTIONS OF A POINT IN FIRST QUADRANT
PICTORIAL
PRESENTATION
PICTORIAL
PRESENTATION
ORTHOGRAPHIC PROJECTIONS
OF ALL ABOVE CASES.
X
Y
a
a´
VP
HP
X
Y
a´
VP
HP
a
X
Y
a
VP
HP
a´
FV above XY,
TV below XY.
FV above XY,
TV on XY.
FV on XY,
TV below XY.

## Slide 8
a´
X
Y
EXAMPLE PROBLEMS ON POINTS
PROBLEM:
A point A is 20 mm above HP and 30 mm in front of VP. Draw its projections
Solution steps:
Draw reference line XY.
Mark a point a´ at a distance of 20 mm above XY.
Through this point draw a perpendicular line to XY and mark the top view a at a distance of 30 mm below XY.
a
30
20
HP
a
VP
A
a´
X
Y
a
20
30
Orthographic projection

## Slide 9
PROBLEM:
Draw the projections of the following points on the same ground line.
Point A, 20 mm above HP, 25 mm behind VP;
(ii) Point B, 25 mm below HP, 20 mm behind VP;
Point C, 20 mm below HP, 30 mm in front of VP;
(iv) Point D, 20 mm above HP, 25 mm in front of VP;
(v) Point E, on HP, 25 mm behind VP;
(vi) Point F, on VP, 30 mm above HP;
X
Y
25
20
a
a´
20
25
c
b
c´
b´
30
20
20
25
d
d´
e
e´
25
30
f
f´
Solution:

## Slide 10
SIMPLE CASES OF THE LINE
A vertical line (line perpendicular to HP & parallel to VP)
Line parallel to both HP & VP.
Line inclined to HP & parallel to VP.
Line inclined to VP & parallel to HP.
Line inclined to both HP & VP.
PROJECTIONS OF STRAIGHT LINES
INFORMATION REGARDING A LINE MEANS:
It’s length
Position of it’s ends with HP & VP
It’s inclinations with HP & VP will be given.
AIM:- To draw it’s projections - means FV & TV.

## Slide 11
X
Y
V.P.
X
Y
V.P.
b´
a´
b
a
F.V.
T.V.
a (b)
a´
b´
B
A
TV
FV
A
B
X
Y
H.P.
V.P.
a´
b´
a (b)
FV
TV
X
Y
H.P.
V.P.
a
b
a´
b´
FV
TV
For FV
For TV
For TV
For FV
Note:
FV is a vertical line
Showing True Length
&
TV is a point.
Note:
FV & TV both are
// to XY
&
both show T. L.
1.
2.
A line
perpendicular
to HP
&
parallel to VP
A line
// to HP
&
// to VP
Orthographic Pattern
Orthographic Pattern
(Pictorial Presentation)
(Pictorial Presentation)

## Slide 12
A line inclined to HP
and
parallel to VP
(Pictorial presentation)
X
Y
V.P.
A
B
b´
a´
b
a


F.V.
T.V.
A line inclined to VP
and
parallel to HP
(Pictorial presentation)
Ø
V.P.
a
b
a´
b´
B
A
Ø
F.V.
T.V.
X
Y
H.P.
V.P.
F.V.
T.V.
a
b
a´
b´

X
Y
H.P.
V.P.
Ø
a
b
a´
b´
TV
FV
TV inclined to XY FV parallel to XY
3.
4.
FV inclined to XY TV parallel to XY
Orthographic Projections

## Slide 13
PROBLEM:
A straight line AB of 40 mm length has one of its ends A, at 10 mm from the HP and 15 mm from the VP. Draw the projections of the line if it is parallel to the VP and inclined at 30° to the HP. Assume the line to be located in each of the four quadrants by turns.
40
30°
X
Y
a
b
a´
b´
15
10
Parallel to VP and inclined to HP
30°
X
Y
a
b
a´
15
10
b´
15
10
X
Y
30°
a
a´
b
b´
10
15
X
Y
a´
a
30°
b
b´
( Quadrant 1)
(Quadrant 2)
(Quadrant 3)
(Quadrant 4)

## Slide 14
X
Y
V.P.
For FV
a´
b´
a
b
B
A


For TV
F.V.
T.V.
X
Y
V.P.
a´
b´
a
b


F.V.
T.V.
For FV
For TV
B
A
X
Y


H.P.
V.P.
a
b
FV
TV
a´
b´
A Line inclined to both
HP and VP
(Pictorial presentation)
5.
Note:-
Both FV & TV are inclined to XY.
(No view is parallel to XY)
Both FV & TV are reduced lengths
(No view shows True Length)
Orthographic Projections
FV is seen on VP clearly.
To see TV clearly, HP is rotated 900 downwards,
Hence it comes below XY.
On removal of object
i.e. Line AB
FV as a image on VP.
TV as a image on HP,

## Slide 15
X
Y
H.P.
V.P.
X
Y

H.P.
V.P.
a
b
TV
a´
b´
FV
TV
b2
b1´
TL
X
Y


H.P.
V.P.
a
b
FV
TV
a´
b´
Here TV (ab) is not // to XY line
Hence it’s corresponding FV
a’ b’ is not showing
True Length &
True Inclination with HP.
In this sketch, TV is rotated
and made // to XY line.
Hence it’s corresponding
FV, a’ b1’ is showing
True Length
&
True Inclination with HP.
Note the procedure
When FV & TV known,
How to find True Length.
(Views are rotated to determine
True Length & it’s inclinations
with HP & VP).
Note the procedure
When True Length is known,
How to locate FV & TV.
(Component a-1 of TL is drawn
which is further rotated
to determine FV)
1
a
a´
b´
1´
b

b1´


TL
b1
Ø
TL
Fv
TV
Orthographic Projections
Means FV & TV of Line AB
are shown below, with their apparent inclinations  & 
Here a -1 is component
of TL ab1 gives length of FV.
Hence it is brought upto
Locus of a’ and further rotated
to get point b’. a’ b’ will be FV.
Similarly drawing component
of other TL (a’ b1‘) TV can be drawn.


## Slide 16
Diagram showing graphical relations
among all important parameters of this topic.
True Length is never rotated. It’s horizontal component is drawn & it is further rotated to locate view.
Views are always rotated, made horizontal & further extended to locate TL,  & Ø
Also remember
TEN important
parameters
to be remembered
with notations
used here onward
Ø



1) True Length (TL) – a’ b1’ & a b1
2) Angle of TL with HP -
3) Angle of TL with VP –
4) Angle of FV with XY –
5) Angle of TV with XY –
6) LTV (length of FV) – Component (a-1)
7) LFV (length of TV) – Component (a’-1’)
8) Position of A- Distances of a & a’ from XY
9) Position of B- Distances of b & b’ from XY
10) Distance between End Projectors
X
Y
H.P.
V.P.
1
a
b

b1
Ø
TL
TV
LFV
a´
b´
1´
b1´

TL
FV

LTV
Distance between
End Projectors.


&
Construct with a’
Ø

&
Construct with a
b & b1 on same locus.
b’ & b1’ on same locus.
NOTE

## Slide 17
a´
b´
a
b
X
Y
b´1
b1
Ø

PROBLEM:
Line AB is 75 mm long and it is 300 & 400 inclined to HP & VP respectively. End A is 12mm above HP and 10 mm in front of VP. Draw projections. Line is in 1st quadrant.
Solution steps:
1) Draw XY line and one projector.
2) Locate a´ 12mm above XY line
& a 10mm below XY line.
3) Take 300 angle from a´ & 400 from a and mark TL, i.e., 75mm on both lines. Name those points b1´ and b respectively.
4) Draw horizontal component of TL a b1 from point b1 and name it 1. (the length a-1 gives length of FV as we have seen already)
5) Extend it up to locus of a and rotating a’ as center locate b´ as shown. Join a´ b´ as FV.
6) From b´ drop a projector downward & get point b. Join a & b, i.e., TV.
LFV
TL
TL
FV
TV
1
INCLINED TO HP & VP

## Slide 18
X
Y
a
a´
b1
450
TL
1
b´ 1
b´
LFV
FV
TL
550
b
TV
PROBLEM:
Line AB 75mm long makes 450 inclination with VP while it’s FV makes 550. End A is 10 mm above HP and 15 mm in front of VP. If line is in 1st quadrant draw it’s projections and find it’s inclination with HP.
LOCUS OF b1
LOCUS OF b1´
Solution Steps:-
1.Draw xy line.
2.Draw one projector for a’ & a
3.Locate a´ 10mm above XY & a 15 mm below XY.
4.Draw a line 450 inclined to XY from point a and cut TL 75 mm on it and name that point b1.
5.Draw locus from point b1.
6.Take 550 angle from a´ for FV above XY line.
7.Draw a vertical line from b1 up to locus of a and name it 1. It is horizontal component of
TL & is LFV.
8.Continue it to locus of a´ and rotate upward up to the line of FV and name it b´. This a´ b´ line is FV.
9. Drop a projector from b´ on locus from point b1 and name intersecting point b. Line ab is TV of line ab.
10.Draw locus from b´ and with TL distance cut point b1´
11.Join a´ b1´ as TL and measure it’s angle α at a´. It will be true angle of line with HP.
α
FINDING INCLINATION WITH HP

## Slide 19
X
a’
Y
a
b’
FV
500
b
600
b1
TL
b’1
TL
PROBLEM: FV of line AB is 500 inclined to XY and measures 55 mm long while its TV is 600 inclined to XY line. If end A is 10 mm above HP and 15 mm in front of VP, draw it’s projections, find TL, inclinations of line with HP & VP.
Solution steps:
1.Draw XY line and one projector.
2.Locate a’ 10 mm above XY and a 15 mm below XY line.
3.Draw locus from these points.
4.Draw FV 500 from a’ and
mark b’ cutting 55mm on it.
5.Similarly draw TV 600 from a & drawing projector from b’
locate point b and join a b.
6.Then rotating views as shown, locate True Lengths ab1 & a’b1’ and their angles with HP and VP.
TV
FINDING TL AND INCLINATIONS

## Slide 20
X
Y
a’
1’
a
b’1
LTV
TL
b1
1
b’
b
LFV
TV
FV

TL

PROBLEM:
Line AB is 75 mm long. It’s FV and TV measure 50 mm & 60 mm long respectively. An end is 10 mm above HP and 15 mm in front of VP. Draw projections of line AB if end B is in first quadrant. Find angle with HP and VP.
SOLUTION STEPS:
1.Draw XY line and one projector.
2.Locate a’ 10 mm above XY and
a 15 mm below XY line.
3.Draw locus from these points.
4.Cut 60mm distance on locus of a’
& mark 1’ on it as it is LTV.
5.Similarly cut 50mm on locus of a
and mark point 1 as it is LFV.
6.From 1’ draw a vertical line upward
and from a’ taking TL (75mm ) in
compass, mark b’1 point on it.
Join a’ b’1 points.
7. Draw locus from b’1
8. With same steps below get b1 point
and draw also locus from it.
9. Now rotating one of the components
i.e., a-1 locate b’ and join a’ with it
to get FV.
10. Locate TV similarly and measure
angles
 and 
FINDING ANGLE WITH HP & VP

## Slide 21
X
Y
c’
c
LOCUS OF d
d
d1
d’1
TV
FV
TL
TL


LOCUS OF d’
PROBLEM: TV of a 75 mm long line CD, measures 50 mm. End C is in HP and 50 mm in front of VP. End D is 15 mm in front of VP and it is above HP. Draw projections of CD and find angles with HP and VP.
SOLUTION STEPS:
1.Draw XY line and one projector.
2.Locate c’ on XY and c 50mm below XY line.
3.Draw locus from these points.
4.Draw locus of d 15 mm below XY.
5.Cut 50mm & 75 mm distances on
locus of d from c and mark points
d & d1 as these are TV and TL. Join both with c.
6.From d1 draw a vertical line upward up to XY i.e., up to locus of c’ and draw an arc as shown.
7 Then draw one projector from d to meet this arc in d’ point & join c’ d’
8. Draw locus of d’ and cut 75 mm
on it from c’ as TL
9.Measure angles
 and 
FINDING ANGLE WITH HP & VP
d’

## Slide 22
TRACES OF THE LINE:-
These are the points of intersections of a line ( or it’s extension ) with respect to reference planes.
A line itself or its extension, where ever touches H.P., that point is called TRACE OF THE LINE ON H.P. (It is called H.T.)
Similarly, a line itself or it’s extension, where ever touches V.P., that point is called TRACE OF THE LINE ON V.P. (it is called V.T.)
V.T.:- It is a point on VP.
Hence it is called FV of a point in VP.
Hence it’s TV comes on XY line.( Here onward denoted as ‘v’)
H.T.:- It is a point on HP.
Hence it is called TV of a point in HP.
Hence it’s FV comes on XY line.( Here onward denoted as ‘h’ )

## Slide 23
Begin with FV. Extend FV up to XY line.
Name this point h’
(as it is a FV of a point in HP)
3. Draw one projector from h’.
4. Now extend TV to meet this projector.
This point is HT
STEPS TO LOCATE HT
(WHEN PROJECTIONS ARE GIVEN)
Begin with TV. Extend TV up to XY line.
Name this point v
(as it is a TV of a point in VP)
3. Draw one projector from v.
4. Now extend FV to meet this projector.
This point is VT
STEPS TO LOCATE VT
(WHEN PROJECTIONS ARE GIVEN)
h’
HT
VT
v
a’
x
Y
a
b’
FV
b
TV
Observe & note :-
1. Points h’ & v always on x-y line.
2. VT & v always on one projector.
3. HT & h’ always on one projector.
4. FV - h’- VT always co-linear.
5. TV - v - HT always co-linear.

## Slide 24: VARIOUS ORIENTATIONS OF THE STRAIGHT LINES
Sl. No. | Orientation/ Position of line | Front view/ Elevation | Top view/ plan | Horizontal trace | Vertical trace
1 | Line parallel to both HP and VP | True length, parallel to xy | True length, parallel to xy | Does not exist | Does not exist
2 | Line perpendicular to HP | True length, perpendicular to xy | Point | Coincides with top view | Does not exist
3 | Line perpendicular to VP | Point | True length, perpendicular to xy | Does not exist | Coincides with front view
4 | Line inclined at Ɵ to HP and parallel to VP | True length inclined at Ɵ to xy | Shorter than the true length, parallel to xy | Exists | Does not exist
5 | Line inclined at Φ to VP and parallel to HP | Shorter than the true length, parallel to xy | True length inclined at Φ to xy | Does not exist | Exists
6 | Line situated in HP and inclined at Φ to VP | Shorter than the true length, lying on xy | True length inclined at Φ to xy | Does not exist | Exists on xy
7 | Line situated in VP and inclined at Ɵ | True length inclined at Ɵ to xy | Shorter than the true length, lying on xy | Exists on xy | Does not exist
8 | Line situated both in HP and VP | Both front and top views are true length and coincide on xy |  | Does not exist | Does not exist