## Slide 1
L-3
ED-ME111
Dr. Poonam Kumari

## Slide 2
SCALES
  A scale is defined as the ratio of the linear dimensions of the object as represented in a drawing to the actual dimensions of the same. The proportion by which the drawing of a given object is enlarged or reduced is called scale of the drawing.
It is not convenient, always, to draw drawings of the object to its actual size. e.g. Buildings, Heavy machines, Bridges, Watches, Electronic devices etc. Thus, following scales are used
Enlargement scales | Reducing/ Reduction scales | Full scale
Scales for the drawing of small objects needs to be enlarged | Scales for the drawing of huge objects needs to be reduced | Object is drawn on sheet to its actual size, then its drawn at full scale.
Format – X:1, X>1, RF>1 | Format – 1:Y, Y>1, RF<1 | Format – 1:1, RF=1
E.g. resistors, screws, gears for electronics, Ics, transistors | E.g. buildings, bridges, boilers, ships, aero planes | E.g. spanner, pen, nut bolts etc.

## Slide 3
RF (Representative Fraction)/ Scale factor
  Ratio that indicates the scale of a drawing is called RF.
REPRESENTATIVE FACTOR (R.F.) =
=
=
=
A
DIMENSION OF DRAWING
DIMENSION OF OBJECT
LENGTH ON DRAWING
ACTUAL LENGTH
AREA OF DRAWING
ACTUAL AREA
VOLUME AS PER DRWG.
ACTUAL VOLUME
V
V
3
For RF above, both the lengths should have same units. All other dimensions of the object should be drawn to the same RF.
Scale and RF are synonymous, as scale is formatted as X:Y, while RF as X/Y.
Format of scale: SCALE X:Y written in the title block. If different objects are drawn to diff. scales on a sheet, respective scale is mentioned below the drawing of that object.
E.g. When a 1 cm long line in a drawing represents 1 meter length of the object,

## Slide 4
BIS (SP 46: 2003) recommended scales
.
Intermediate scales can be used in exceptional cases where recommended scales can not be applied for functional reasons.
LOS (Length of Scale) (mm)
All the scales (except the scale of chords) are constructed by drawing a line of length equivalent to the actual distance to be represented. This length is called length of scale (LOS).
LENGTH OF SCALE (LOS)= R.F. X MAX. LENGTH TO BE MEASURED.

## Slide 5
Types of scale
.
• Engineers Scale :
The relation between the dimension on the drawing and the actual dimension of the object is mentioned numerically (like 10mm = 15 m).
• Graphical Scale:
Scale is drawn on the drawing itself. This takes care of the shrinkage of the engineer’s scale when the drawing becomes old.
Types of scales
PLAIN SCALES ( FOR DIMENSIONS UP TO SINGLE DECIMAL)
DIAGONAL SCALES ( FOR DIMENSIONS UP TO TWO DECIMALS)
VERNIER SCALES ( FOR DIMENSIONS UP TO TWO DECIMALS)
COMPARATIVE SCALES ( FOR COMPARING TWO DIFFERENT UNITS)
SCALE OF CORDS ( FOR MEASURING/CONSTRUCTING ANGLES)

## Slide 6
Procedure to construct scales
.
Calculate RF, if not given
Calculate LOS
If the maximum distance to be represented is not known, it may be taken equal to the maximum measurement (rounded off to the higher whole number) to be made with the help of scale.
Draw a line = LOS. Divide this line into the required number of equal parts. The divisions thus obtained are main divisions. Each main division will indicate the main unit of measurement. In case of speed or rate the same scale can be used for both time and distance.
Mark zero at the end of the first main division. Number the main divisions rightward from zero.
Divide the first main division into the required number of equal parts. The subdivisions obtained indicates subunits of the main unit. Number the subdivisions leftward from zero. Main unit is written below the right end of the scale and the subunit below the first main division. RF should be mentioned below the scale.

## Slide 7
PLAIN SCALES ( FOR DIMENSIONS UP TO SINGLE DECIMAL)
DIAGONAL SCALES ( FOR DIMENSIONS UP TO TWO DECIMALS)
VERNIER SCALES ( FOR DIMENSIONS UP TO TWO DECIMALS)
COMPARATIVE SCALES ( FOR COMPARING TWO DIFFERENT UNITS)
SCALE OF CORDS ( FOR MEASURING/CONSTRUCTING ANGLES)
TYPES OF SCALES:
= 10 HECTOMETRES
= 10 DECAMETRES
= 10 METRES
= 10 DECIMETRES
= 10 CENTIMETRES
= 10 MILIMETRES
1 KILOMETRE
1 HECTOMETRE
1 DECAMETRE
1 METRE
1 DECIMETRE
1 CENTIMETRE
BE FRIENDLY WITH THESE UNITS.

## Slide 8
Plain scales
.
A plain scale consists of a line divided into suitable number of equal units. The first unit is subdivided into smaller parts.
The plain scales give only two dimensions, such as a unit and it’s subunit or it’s fraction.
• The zero should be placed at the end of the 1st main unit.
• From the zero mark, the units should be numbered to the right and the sub-divisions to the left.
• The units and the subdivisions should be labelled clearly.
• The R.F. should be mentioned below the scale.

## Slide 9
0
1
2
3
4
5
10
PLAIN SCALE:-
This type of scale represents two units or a unit and it’s sub-division.
METERS
DECIMETERS
R.F. = 1/100
4 M 6 DM
PLANE SCALE SHOWING METERS AND DECIMETERS.
PLAIN SCALE
PROBLEM NO.1:- Draw a scale 1 cm = 1m to read decimeters, to measure maximum distance of 6 m.
Show on it a distance of 4 m and 6 dm.
CONSTRUCTION:-
a) Calculate R.F.=
R.F.= 1cm/ 1m = 1/100
Length of scale = R.F. X max. distance
= 1/100 X 600 cm
= 6 cms
b) Draw a line 6 cm long and divide it in 6 equal parts. Each part will represent larger division unit.
c) Sub divide the first part which will represent second unit or fraction of first unit.
d) Place ( 0 ) at the end of first unit. Number the units on right side of Zero and subdivisions
on left-hand side of Zero. Take height of scale 5 to 10 mm for getting a look of scale.
e) After construction of scale mention it’s RF and name of scale as shown.
f) Show the distance 4 m 6 dm on it as shown.
DIMENSION OF DRAWING
DIMENSION OF OBJECT

## Slide 10
PROBLEM NO.2:- In a map a 36 km distance is shown by a line 45 cms long. Calculate the R.F. and construct
a plain scale to read kilometers and hectometers, for max. 12 km. Show a distance of 8.3 km on it.
CONSTRUCTION:-
a) Calculate R.F.
R.F.= 45 cm/ 36 km = 45/ 36 . 1000 . 100 = 1/ 80,000
Length of scale = R.F. max. distance
= 1/ 80000 12 km
= 15 cm
b) Draw a line 15 cm long and divide it in 12 equal parts. Each part will represent larger division unit.
c) Sub divide the first part which will represent second unit or fraction of first unit.
d) Place ( 0 ) at the end of first unit. Number the units on right side of Zero and subdivisions
on left-hand side of Zero. Take height of scale 5 to 10 mm for getting a look of scale.
e) After construction of scale mention it’s RF and name of scale as shown.
f) Show the distance 8.3 km on it as shown.
KILOMETERS
HECTOMETERS
8KM 3HM
R.F. = 1/80,000
PLANE SCALE SHOWING KILOMETERS AND HECTOMETERS
0
1
2
3
4
5
6
7
8
9
10
11
10
5
PLAIN SCALE

## Slide 11
PROBLEM NO.3:- The distance between two stations is 210 km. A passenger train covers this distance
in 7 hours. Construct a plain scale to measure time up to a single minute. RF is 1/200,000 Indicate the distance
traveled by train in 29 minutes.
CONSTRUCTION:-
a) 210 km in 7 hours. Means speed of the train is 30 km per hour ( 60 minutes)
Length of scale = R.F. max. distance per hour
= 1/ 2,00,000 30km
= 15 cm
b) 15 cm length will represent 30 km and 1 hour i.e. 60 minutes.
Draw a line 15 cm long and divide it in 6 equal parts. Each part will represent 5 km and 10 minutes.
c) Sub divide the first part in 10 equal parts,which will represent second unit or fraction of first unit.
Each smaller part will represent distance traveled in one minute.
d) Place ( 0 ) at the end of first unit. Number the units on right side of Zero and subdivisions
on left-hand side of Zero. Take height of scale 5 to 10 mm for getting a proper look of scale.
e) Show km on upper side and time in minutes on lower side of the scale as shown.
After construction of scale mention it’s RF and name of scale as shown.
f) Show the distance traveled in 29 minutes, which is 14.5 km, on it as shown.
PLAIN SCALE
0
10
20
30
40
50
10
MINUTES
MIN
R.F. = 1/100
PLANE SCALE SHOWING METERS AND DECIMETERS.
KM
KM
0
5
10
15
20
25
5 2.5
DISTANCE TRAVELED IN 29 MINUTES.
14.5 KM

## Slide 12
Diagonal scales
.
Through Diagonal scale, measurements can be up to second decimal places (e.g. 4.35).
Are used to measure distances in a unit and its immediate two subdivisions; e.g. dm, cm & mm, or yard, foot & inch.
Diagonal scale can measure more accurately than the plain scale.
Concept (based on similarity of triangles)
At end B of line AB, draw a perpendicular.
Step-off ten equal divisions of any length along
the perpendicular starting from B and ending at C.
Number the division points 9,8,7,…..1.
Join A with C.
Through the points 1, 2, 3, etc., draw lines parallel to AB and cutting AC at 1΄, 2΄, 3΄, etc.

## Slide 13
Diagonal scales
.
Since the triangles are similar; 1΄1 = 0.1 AB,
2΄2 = 0.2AB, …. 9΄9 = 0.9AB.
Gives divisions of a given short line AB in
multiples of 1/10 its length,
e.g. 0.1AB, 0.2AB, 0.3AB, etc.

## Slide 14
R.F. = 1 / 40,00,000
DIAGONAL SCALE SHOWING KILOMETERS.
0
100
200
300
400
500
100
50
10
9
8
7
6
5
4
3
2
1
0
KM
KM
KM
569 km
459 km
336 km
222 km
PROBLEM NO. 4 : The distance between Delhi and Agra is 200 km.
In a railway map it is represented by a line 5 cm long. Find it’s R.F.
Draw a diagonal scale to show single km. And maximum 600 km.
Indicate on it following distances. 1) 222 km 2) 336 km 3) 459 km 4) 569 km
SOLUTION STEPS: RF = 5 cm / 200 km = 1 / 40, 00, 000
Length of scale = 1 / 40, 00, 000 X 600 X 105 = 15 cm
Draw a line 15 cm long. It will represent 600 km.Divide it in six equal parts.( each will represent 100 km.)
Divide first division in ten equal parts.Each will represent 10 km.Draw a line upward from left end and
mark 10 parts on it of any distance. Name those parts 0 to 10 as shown.Join 9th sub-division of horizontal scale
with 10th division of the vertical divisions. Then draw parallel lines to this line from remaining sub divisions and
complete diagonal scale.
DIAGONAL
SCALE

## Slide 15
PROBLEM NO.5: A rectangular plot of land measuring 1.28 hectors is represented on a map by a similar rectangle
of 8 sq. cm. Calculate RF of the scale. Draw a diagonal scale to read single meter. Show a distance of 438 m on it.
Draw a line 15 cm long.
It will represent 600 m.Divide it in six equal parts.
( each will represent 100 m.)
Divide first division in ten equal parts.Each will
represent 10 m.
Draw a line upward from left end and
mark 10 parts on it of any distance.
Name those parts 0 to 10 as shown.Join 9th sub-division
of horizontal scale with 10th division of the vertical divisions.
Then draw parallel lines to this line from remaining sub divisions
and complete diagonal scale.
DIAGONAL
SCALE
SOLUTION :
1 hector = 10, 000 sq. meters
1.28 hectors = 1.28 X 10, 000 sq. meters
= 1.28 X 104 X 104 sq. cm
8 sq. cm area on map represents
= 1.28 X 104 X 104 sq. cm on land
1 cm sq. on map represents
= 1.28 X 10 4 X 104 / 8 sq cm on land
1 cm on map represent
=
1.28 X 10 4 X 104 / 8
cm
= 4, 000 cm
1 cm on drawing represent 4, 000 cm, Means RF = 1 / 4000
Assuming length of scale 15 cm, it will represent 600 m.
0
100
200
300
400
500
100
50
10
9
8
7
6
5
4
3
2
1
0
M
M
M
438 meters
R.F. = 1 / 4000
DIAGONAL SCALE SHOWING METERS.

## Slide 16
10
9
8
7
6
5
4
3
2
1
0
CENTIMETRES
MM
CM
R.F. = 1 / 2.5
DIAGONAL SCALE SHOWING CENTIMETERS.
0
5
10
15
5
4
3
2
1
PROBLEM NO.6:. Draw a diagonal scale of R.F. 1: 2.5, showing centimeters
and millimeters and long enough to measure up to 20 centimeters.
SOLUTION STEPS:
R.F. = 1 / 2.5
Length of scale = 1 / 2.5 X 20 cm.
= 8 cm.
1.Draw a line 8 cm long and divide it in to 4 equal parts.
(Each part will represent a length of 5 cm.)
2.Divide the first part into 5 equal divisions.
(Each will show 1 cm.)
3.At the left hand end of the line, draw a vertical line and
on it step-off 10 equal divisions of any length.
4.Complete the scale as explained in previous problems.
Show the distance 13.4 cm on it.
13 .4 CM
DIAGONAL
SCALE

## Slide 17
COMPARATIVE SCALES:
These are the Scales having same R.F.
but graduated to read different units.
These scales may be Plain scales or Diagonal scales
and may be constructed separately or one above the other.
EXAMPLE NO. 7 :
A distance of 40 miles is represented by a line
8 cm long. Construct a plain scale to read 80 miles.
Also construct a comparative scale to read kilometers
upto 120 km ( 1 m = 1.609 km )
SOLUTION STEPS:
Scale of Miles:
40 miles are represented = 8 cm
: 80 miles = 16 cm
R.F. = 8 / 40 X 1609 X 1000 X 100
= 1 / 8, 04, 500
CONSTRUCTION:
Take a line 16 cm long and divide it into 8 parts. Each will represent 10 miles.
Subdivide the first part and each sub-division will measure single mile.
Scale of Km:
Length of scale
= 1 / 8,04,500 X 120 X 1000 X 100
= 14. 90 cm
CONSTRUCTION:
On the top line of the scale of miles cut off a distance of 14.90 cm and divide
it into 12 equal parts. Each part will represent 10 km.
Subdivide the first part into 10 equal parts. Each subdivision will show single km.
10
10
0
20
30
5
50
60
70 MILES
40
10
0
10
20
30
40
50
60
70
80
90
100
110 KM
5
R.F. = 1 / 804500
COMPARATIVE SCALE SHOWING MILES AND KILOMETERS

## Slide 18
COMPARATIVE SCALE:
EXAMPLE NO. 8 :
A motor car is running at a speed of 60 kph.
On a scale of RF = 1 / 4,00,000 show the distance
traveled by car in 47 minutes.
SOLUTION STEPS:
Scale of km.
length of scale = RF X 60 km
= 1 / 4,00,000 X 60 X 105
= 15 cm.
CONSTRUCTION:
Draw a line 15 cm long and divide it in 6 equal parts.
( each part will represent 10 km.)
Subdivide 1st part in `0 equal subdivisions.
( each will represent 1 km.)
Time Scale:
Same 15 cm line will represent 60 minutes.
Construct the scale similar to distance scale.
It will show minimum 1 minute & max. 60min.
10
10
0
20
30
5
50 KM
40
10
10
0
20
30
5
50 MINUTES
40
MIN.
KM
47 MINUTES
47 KM
R.F. = 1 / 4,00,000
COMPARATIVE SCALE SHOWING MINUTES AND KILOMETERS

## Slide 19
EXAMPLE NO. 9 :
A car is traveling at a speed of 60 km per hour. A 4 cm long line represents the distance traveled by the car in two hours.
Construct a suitable comparative scale up to 10 hours. The scale should be able to read the distance traveled in one minute.
Show the time required to cover 476 km and also distance in 4 hours and 24 minutes.
COMPARATIVE
SCALE:
SOLUTION:
4 cm line represents distance in two hours , means for 10 hours scale, 20 cm long line is required, as length
of scale.This length of scale will also represent 600 kms. ( as it is a distance traveled in 10 hours)
CONSTRUCTION:
Distance Scale ( km)
Draw a line 20 cm long. Divide it in TEN equal parts.( Each will show 60 km)
Sub-divide 1st part in SIX subdivisions.( Each will represent 10 km)
At the left hand end of the line, draw a vertical line and on it step-off 10 equal divisions of any length.
And complete the diagonal scale to read minimum ONE km.
Time scale:
Draw a line 20 cm long. Divide it in TEN equal parts.( Each will show 1 hour) Sub-divide 1st part in SIX subdivisions.( Each will
represent 10 minutes) At the left hand end of the line, draw a vertical line and on it step-off 10 equal divisions of any length.
And complete the diagonal scale to read minimum ONE minute.
10
5
0
kM
kM
0
60
60
120
180
240
300
360
420
480
540
0
60
1
2
3
4
5
6
7
8
9 HOURS
MIN.
10
5
0
KILOMETERS
DISTANCE SCALE TO MEASURE MIN 1 KM
TIME SCALE TO MEASURE MIN 1 MINUTE.
4 hrs 24 min. ( 264 kms )
476 kms ( 7 hrs 56 min.)

## Slide 20
Vernier scales
.
Similar to Diagonal scale, Vernier scale is used for measuring up to second decimal.
A Vernier scale consists of (i) a primary scale and (ii) vernier.
The primary scale is a plain scale fully divided in to minor divisions. Subdivision on main scale is called main scale div.
The graduations on the vernier are derived from those on the primary scale. Subdivision - vernier scale division (VSD).
Vernier is auxillary scale above main scale whose length can be more or less by fixed amount than that of main div.
Least count (LC)
It is the minimum
distance that can be
measured precisely
by a given vernier scale.

## Slide 21
Figure to the right shows a part of a plain scale in
which length A-O represents 10 cm. If we divide A-O
into ten equal parts, each will be of 1 cm. Now it would
not be easy to divide each of these parts into ten equal
divisions to get measurements in millimeters.
Now if we take a length BO equal to 10 + 1 = 11 such equal parts, thus representing 11 cm, and divide it into ten equal divisions, each of these divisions will represent 11 / 10 – 1.1 cm.
The difference between one part of AO and one division of BO will be equal 1.1 – 1.0 = 0.1 cm or 1 mm.
This difference is called Least Count of the scale.
Minimum this distance can be measured by this scale.
The upper scale BO is the vernier.The combination of plain scale and the vernier is vernier scale.
Vernier Scales:
These scales, like diagonal scales , are used to read to a very small unit with great accuracy.
It consists of two parts – a primary scale and a vernier. The primary scale is a plain scale fully
divided into minor divisions.
As it would be difficult to sub-divide the minor divisions in ordinary way, it is done with the help of the vernier.
The graduations on vernier are derived from those on the primary scale.
9.9
7.7
5.5
3.3
1.1
9
8
7
6
5
4
3
2
1
0
A
0
B

## Slide 22
Determination of LC
.
This can be determined by the following expression: LC = MSD – VSD ( if MSD > VSD) – forward vernier scale LC = VSD – MSD ( if VSD > MSD) - backward vernier scale
The LC is mentioned as a fraction of the MSD. If the MSD of a scale represents 1 mm and LC is 0.1 mm,
LC = 0.1 mm = (1/10) MSD
Case of forward scale
Assume MSD > VSD LC = MSD –VSD 1/10 MSD = MSD –VSD i.e., VSD = MSD – 1/10 MSD 10 VSD = 9 MSD i.e., Length of VSD = 9 MSD.
This length must be divided in to 10 equal parts so that LC = 0.1 mm

## Slide 23
Determination of LC…..
.
Case of backward scale
Assume VSD > MSD LC = VSD – MSD 1/10 MSD = VSD – MSD i.e., VSD = 1/10 MSD + MSD 10 VSD = 11 MSD This length is to be divided in to 20 equal parts so that LC = 0.1 mm
Concept of vernier scale
Length A0 represents 10 cm
& is divided in to 10 equal parts
each representing 1 cm.
B0 = 11 (i.e. 10+1) such equal parts = 11 cm.
Divide B0 into 10 equal divisions. Each division of B0 will be equal to 11/10 = 1.1 cm or 11 mm.
Difference between 1 part of A0 and one part of B0 =
1.1 cm -1.0cm = 0.1cm or 1 mm. (least count of the scale)

## Slide 24
Example 10:
Draw a vernier scale of RF = 1 / 25 to read centimeters upto
4 meters and on it, show lengths 2.39 m and 0.91 m
.9
.8
.7
.6
.5
.4
.3
.2
.1
.99
.77
.55
.33
.11
0
1.1
0
1
2
3
1.0
SOLUTION:
Length of scale = RF X max. Distance
= 1 / 25 X 4 X 100
= 16 cm
CONSTRUCTION: ( Main scale)
Draw a line 16 cm long.
Divide it in 4 equal parts.
( each will represent meter )
Sub-divide each part in 10 equal parts.
( each will represent decimeter )
Name those properly.
CONSTRUCTION: ( vernier)
Take 11 parts of Dm length and divide it in 10 equal parts.
Each will show 0.11 m or 1.1 dm or 11 cm and construct a rectangle
Covering these parts of vernier.
TO MEASURE GIVEN LENGTHS:
(1) For 2.39 m : Subtract 0.99 from 2.39 i.e. 2.39 - .99 = 1.4 m
The distance between 0.99 ( left of Zero) and 1.4 (right of Zero) is 2.39 m
(2) For 0.91 m : Subtract 0.11 from 0.91 i.e. 0.91 – 0.11 =0.80 m
The distance between 0.11 and 0.80 (both left side of Zero) is 0.91 m
1.4
2.39 m
0.91 m
METERS
METERS
Vernier Scale

## Slide 25
Example 11: A map of size 500cm X 50cm wide represents an area of 6250 sq.Kms.
Construct a vernier scaleto measure kilometers, hectometers and decameters
and long enough to measure upto 7 km. Indicate on it a) 5.33 km b) 59 decameters.
Vernier Scale
SOLUTION:
RF =
=
= 2 / 105
Length of
scale = RF X max. Distance
= 2 / 105 X 7 kms
= 14 cm
AREA OF DRAWING
ACTUAL AREA
V
500 X 50 cm sq.
6250 km sq.
V
CONSTRUCTION: ( vernier)
Take 11 parts of hectometer part length
and divide it in 10 equal parts.
Each will show 1.1 hm m or 11 dm and
Covering in a rectangle complete scale.
CONSTRUCTION: ( Main scale)
Draw a line 14 cm long.
Divide it in 7 equal parts.
( each will represent km )
Sub-divide each part in 10 equal parts.
( each will represent hectometer )
Name those properly.
KILOMETERS
HECTOMETERS
0
1
2
3
10
4
5
6
90
70
50
30
10
99
77
55
33
11
Decameters
TO MEASURE GIVEN LENGTHS:
a) For 5.33 km :
Subtract 0.33 from 5.33
i.e. 5.33 - 0.33 = 5.00
The distance between 33 dm
( left of Zero) and
5.00 (right of Zero) is 5.33 k m
(b) For 59 dm :
Subtract 0.99 from 0.59
i.e. 0.59 – 0.99 = - 0.4 km
( - ve sign means left of Zero)
The distance between 99 dm and
- .4 km is 59 dm
(both left side of Zero)
5.33 km
59 dm

## Slide 26
100
200
300
400
500
600
700
800
900
00
0
10
20
40
30
70
50
60
90
80
SCALE OF CORDS
O
A
CONSTRUCTION:
1. DRAW SECTOR OF A CIRCLE OF 900 WITH ‘OA’ RADIUS.
( ‘OA’ ANY CONVINIENT DISTANCE )
2. DIVIDE THIS ANGLE IN NINE EQUAL PARTS OF 10 0 EACH.
3. NAME AS SHOWN FROM END ‘A’ UPWARDS.
4. FROM ‘A’ AS CENTER, WITH CORDS OF EACH ANGLE AS RADIUS
DRAW ARCS DOWNWARDS UP TO ‘AO’ LINE OR IT’S EXTENSION
AND FORM A SCALE WITH PROPER LABELING AS SHOWN.
AS CORD LENGTHS ARE USED TO MEASURE & CONSTRUCT
DIFERENT ANGLES IT IS CALLED SCALE OF CORDS.

## Slide 27
100
200
300
400
500
600
700
800
900
00
0
10
20
40
30
70
50
60
90
80
O
A
O
A
B
O1
A1
B1
x
z
y
PROBLEM 12: Construct any triangle and measure it’s angles by using scale of cords.
CONSTRUCTION:
First prepare Scale of Cords for the problem.
Then construct a triangle of given sides. ( You are supposed to measure angles x, y and z)
To measure angle at x:
Take O-A distance in compass from cords scale and mark it on lower side of triangle
as shown from corner x. Name O & A as shown. Then O as center, O-A radius
draw an arc upto upper adjacent side.Name the point B.
Take A-B cord in compass and place on scale of cords from Zero.
It will give value of angle at x
To measure angle at y:
Repeat same process from O1. Draw arc with radius O1A1.
Place Cord A1B1 on scale and get angle at y.
To measure angle at z:
Subtract the SUM of these two angles from 1800 to get angle at z.
SCALE OF CORDS
0
10
20
40
30
70
50
60
90
80
0
10
20
40
30
70
50
60
90
80
300
550
Angle at z = 180 – ( 55 + 30 ) = 950

## Slide 28
100
200
300
400
500
600
700
800
900
00
0
10
20
40
30
70
50
60
90
80
O
A
PROBLEM 12: Construct 250 and 1150 angles with a horizontal line , by using scale of cords.
CONSTRUCTION:
First prepare Scale of Cords for the problem.
Then Draw a horizontal line. Mark point O on it.
To construct 250 angle at O.
Take O-A distance in compass from cords scale and mark it on on the line drawn, from O
Name O & A as shown. Then O as center, O-A radius draw an arc upward..
Take cord length of 250 angle from scale of cords in compass and
from A cut the arc at point B.Join B with O. The angle AOB is thus 250
To construct 1150 angle at O.
This scale can measure or construct angles upto 900 only directly.
Hence Subtract 1150 from 1800.We get 750 angle ,
which can be constructed with this scale.
Extend previous arc of OA radius and taking cord length of 750 in compass cut this arc
at B1 with A as center. Join B1 with O. Now angle AOB1 is 750 and angle COB1 is 1150.
SCALE OF CORDS
B1
750
1150
0
10
20
40
30
70
50
60
90
80
B
250
0
10
20
40
30
70
50
60
90
80
A
O
O
C
A
To construct 250 angle at O.
To construct 1150 angle at O.

## Slide 29
Example: A map of size 500cm X 50cm wide represents an area of 6250 sq.Kms.
Construct a vernier scale to measure kilometers, hectometers and decameters
and long enough to measure upto 7 km. Indicate on it a) 5.33 km b) 59 decameters.
Vernier Scale
SOLUTION:
RF =
=
= 2 / 105
Length of
scale = RF X max. Distance
= 2 / 105 X 7 kms
= 14 cm
AREA OF DRAWING
ACTUAL AREA
V
500 X 50 cm sq.
6250 km sq.
V
CONSTRUCTION: ( vernier)
Take 11 parts of hectometer part length
and divide it in 10 equal parts.
Each will show 1.1 hm m or 11 dm and
Covering in a rectangle complete scale.
CONSTRUCTION: ( Main scale)
Draw a line 14 cm long.
Divide it in 7 equal parts.
( each will represent km )
Sub-divide each part in 10 equal parts.
( each will represent hectometer )
Name those properly.
KILOMETERS
HECTOMETERS
0
1
2
3
10
4
5
6
90
70
50
30
10
99
77
55
33
11
Decameters
TO MEASURE GIVEN LENGTHS:
a) For 5.33 km :
Subtract 0.33 from 5.33
i.e. 5.33 - 0.33 = 5.00
The distance between 33 dm
( left of Zero) and
5.00 (right of Zero) is 5.33 k m
(b) For 59 dm :
Subtract 0.99 from 0.59
i.e. 0.59 – 0.99 = - 0.4 km
( - ve sign means left of Zero)
The distance between 99 dm and
- .4 km is 59 dm
(both left side of Zero)
5.33 km
59 dm