## Slide 1: Orthographic VIEWS

## Slide 2: Orthographic Projections
Orthographic Projections is a technical drawing in which different views of an object are projected on different reference planes observing perpendicular to respective reference plane.
Different reference planes are:
  Horizontal Plane (HP)
  Vertical Plane (VP)
  Side or Profile Plane (PP)
Different views are:
  Front View (FV) – Projected on VP
  Top View (TV) – Projected on HP
  Side View (SV) – Projected on PP

## Slide 3
NOTATIONS
Following notations are followed while naming
different views in orthographic projections:
IT’S FRONT VIEW a´ a´ b´
Same system of notations should be followed
in case numbers, like 1, 2, 3 – are used.
OBJECT POINT A LINE AB
IT’S TOP VIEW a a b
IT’S SIDE VIEW a´´ a´´ b´´
TERMS ‘ABOVE’ & ‘BELOW’ WITH RESPECT TO H.P.
AND TERMS ‘IN FRONT’ & ‘BEHIND’ WITH RESPECT TO V.P.

## Slide 4
Types of views
Projections
Converge
Parallel
Orthogonal
Oblique
Axonometric
Multiview
Pictorial drawing
Perspective drawing
Multi-view drawing

## Slide 5
View comparison
Pictorial drawing
Perspective drawing
Multi-view drawing
Difficult to create
Easy to visualize.
Shape and angle distortion
Object looks more like what our eyes
perceive.
Size and shape distortion
Right angle becomes obtuse angle.
Circular hole becomes ellipse
Distorted
width
Accurately presents object’s details, i.e.
size and shape.
Require training
for visualization.
Advantage
Disadvantage
Type
Front View
Right Side View
Top View

## Slide 6

A.I.P.
 to Vp
&
 to Hp

A.V.P.
 to Hp &  to Vp
PLANES
PRINCIPAL PLANES
HP AND VP
AUXILIARY PLANES
Auxiliary Vertical Plane
(A.V.P.)
Profile Plane
( P.P.)
Auxiliary Inclined Plane
(A.I.P.)

## Slide 7
THIS IS A PICTORIAL SET-UP OF ALL THREE PLANES.
ARROW DIRECTION IS A NORMAL WAY OF OBSERVING THE OBJECT.
BUT IN THIS DIRECTION ONLY VP AND A VIEW ON IT (FV) CAN BE SEEN.
THE OTHER PLANES AND VIEWS ON THOSE CAN NOT BE SEEN.
X
Y
HP IS ROTATED DOWNWARD 900
AND
BROUGHT IN THE PLANE OF VP.
PP IS ROTATED IN RIGHT SIDE 900
AND
BROUGHT IN THE PLANE OF VP.
X
Y
X
Y
VP
HP
PP
FV
ACTUAL PATTERN OF PLANES & VIEWS
OF ORTHOGRAPHIC PROJECTIONS
DRAWN IN
FIRST ANGLE METHOD OF PROJECTIONS
LSV
TV
PROCEDURE TO SOLVE ABOVE PROBLEM:-
TO MAKE THOSE PLANES ALSO VISIBLE FROM THE ARROW DIRECTION,
A) HP IS ROTATED 900 DOWNWARD
B) PP, 900 IN RIGHT SIDE DIRECTION.
THIS WAY BOTH PLANES ARE BROUGHT IN THE SAME PLANE CONTAINING VP.
PATTERN OF PLANES & VIEWS (First Angle Method)

## Slide 8
Projection systems
1. First angle system
2. Third angle system
First
quadrant
Third
quadrant
- European countries - ISO standard
- Canada, USA, Japan, Thailand
Transparent
planes
Opaque
planes

## Slide 9
1st angle system
(Opaque planes)
3rd angle system
(transparent planes/glass box)
Orthographic views

## Slide 10
Folding
line
Folding
line
Folding
line
Folding
line


1st angle system
3rd angle system
Orthographic views

## Slide 11
1st angle system
3rd angle system
Front View
Front View
Right Side View
Right Side View
Top View
Top View
Views arrangement

## Slide 12
Projection symbols
1st angle system
3rd angle system
d
1.7d
2.2d

## Slide 13
1. Natural Method: Revolve the object with respect to observer
Methods of Orthogonal Projection
2. Glass box method: The observer moves around the object.
Front view
Right side view
Top view
Right side
view
Top view
play
play
Front
view
Glass box concept

## Slide 14
Glass box : Revolution of the planes of projection
Bottom view
Left side view
Rear view

## Slide 15
Height
Width
Depth
Relative orientation of views
Left side view
Right side view
Bottom view
Top view
Rear view
Front view

## Slide 16
Summary : Problem solving steps
1
2
3
4
Given

## Slide 17
Steps for Orthographic Views
1. Select the necessary views
2. Layout the selected views on a drawing sheet.
3. Complete each selected views.
4. Complete the
dimensions and notes.
45
152
152
64
25~40
Front
Top
Choose a drawing scale
(say 1:1)
Front
Top
y
y
x
x
x
x
y
y
z

## Slide 18
Procedures for View Selection
1. Orient the object to the best position relative to a glass box.
2. Select the front view.
3. Select adjacent views.

## Slide 19
Suggestions: Orient the object
1. The object should be placed in its natural position.
NO !
2. The orthographic views should represent the true size and true shape of an object (as much as possible).
GOOD

## Slide 20
Suggestions: Select the front view
1. The longest dimension of an object should be presented as a width (in a front view).
Inappropriate
First choice
Good
Second choice
Use more space

## Slide 21
Inappropriate
2. The adjacent views project from the selected front view should be appeared in a natural position.
Suggestions: Select the front view

## Slide 22
3. It has the fewest number of hidden lines.
Good
Inappropriate
Suggestions: Select the front view

## Slide 23
Suggestions: Select an adjacent view
Inappropriate
Inappropriate
1. Choose the view that has the fewest number of hidden lines.

## Slide 24
2. Choose the minimum number of views that can represent the major features of the object.
Necessary
Necessary
Hole’s information is placed on a separated view.
Suggestions: Select an adjacent view
All information is placed
on a single view.

## Slide 25
3. Choose the views that are suitable to a drawing sheet.
Good
Suggestions: Select an adjacent view
Poor
Not enough space
for dimensioning.
Good
Choose another adjacent view.
Change orientation of the
selected views.

## Slide 26
Summary
View selection has 3 steps
Orient
the object
Select
front view
Select
adjacent views

## Slide 27
Object that requires only one-view
Flat (thin) part having a uniform thickness such as a gasket, sheet metal etc.
Adjacent views provide only a
part’s thickness !
1 Thick
Cylindrical-shaped part.
Example

## Slide 28
Repeat !
Infer from CL
Object that requires only one-view
Example
Example
Flat (thin) part having a uniform thickness such as a gasket, sheet metal etc.
Cylindrical-shaped part.

## Slide 29
Identical adjacent view exists.
Repeat !
Object that requires only two-view
The 3rd view has no significant contours of the object.
(provides no additional information)
Example

## Slide 30
Object that requires only two-view
Identical view exists.
Example 1
The 3rd view has no significant contours of the object.
(provides no additional information)

## Slide 31
Object that requires only two-view
Identical view exists.
Example 2
The 3rd view has no significant contours of the object.
(provides no additional information)

## Slide 32: Example
Identify surfaces perpendicular or inclined to the view
Surfaces parallel to the view would not be visible in that view.
First draw horizontal and vertical reference planes (easily identifiable on drawing)
Start drawing from the reference planes.
Steps to draw projections

## Slide 33
Side view
Front view
Top view
Horizontal reference plane (HP)
Vertical reference plane (VP)

## Slide 34
HP
VP
Front view
Side view
Top view
80+40+80=200
50
70
Φ 50
30+20=50
Midpoint
35
80
40
70
20

## Slide 35
200
Φ 50
50
80
40
70
20
Front view
Side view
Top view
80
70
125
50
25
20
25
+

## Slide 36
x
y
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
FOR F.V.
FOR S.V.
FOR T.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
F.V.
S.V.
Example

## Slide 37
FOR T.V.
FOR S.V.
F.V.
S.V.
ORTHOGRAPHIC PROJECTIONS
FOR F.V.
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
Example

## Slide 38
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
S.V.
F.V.
FOR T.V.
FOR F.V.
FOR S.V.
ORTHOGRAPHIC PROJECTIONS
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
Example

## Slide 39
Example
x
y
FV
35
35
10
TV
30
20
10
40
70
O
FOR T.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND TV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS

## Slide 40
450
X
FV
Y
30
40
TV
30 D
40
40
15
O
FOR T.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND TV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
Example

## Slide 41
FOR T.V.
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
Example